## Slide 1: A Network-aware Job Management System Leveraging Software Defined Networking
Yasuhiro Watashiba
Cybermedia Center, Osaka University, Japan

## Slide 2: Cluster system with OpenFlow network
Interconnect in the cluster system will be constructed as OpenFlow network.
  OpenFlow switches : HP 2920-24G
  Topology of the interconnect has multi paths.
OpenFlow network
Computational hosts
PRAGMA ENT

## Slide 3: Network Resource Management
  User interface to request network resources
  Monitoring and managing status of network resources
  Allocation control for network resources
  Policy to determine appropriate allocation of resources
Job script
JMS
Computing resources
SW
SW
SW
SW
SW
SW
SW
Network resources
(2)
(3)
(1)
User
Administrator
Policy
(4)
Notes: In order to manage and allocate network resources by JMS, we think that 4 functionalities for handling network resources are necessary.
The 1st functionality is user interface to request network resources in a job script.
This functionality allows a user to request network resources as well as computing resources in submitting user job.
The 2nd functionality is monitoring the network condition and managing their information.
This functionality makes JMS possible to understand current status of network resources in computing environment.
In order to control network resources, we consider that this module need to be able to retrieve network topology and the capacity on each network link, such as bandwidth and latency.
The 3rd functionality is allocation control for network resources.
This functionality is necessary to share network resources with user jobs which are executed at the same time so that each of user jobs can obtain the better performance.
The 4th functionality is a framework for a resource assignment policy to determine an appropriate allocation of network and computing resources to a job.
Since traditional JMSs do not have a functionality to configure assignment rule for network resource, it is necessary to provide the interface to administrator.

## Slide 4: Application for resource management
  Leveraging Software Defined Networking / OpenFlow
  Retrieving information of network resources
  Managing and allocating network flows on each job
Network Management Module (NMM)
Database
Brain
Network Control
OpenFlow Controller (Trema)
SDN-based JMS Framework
Resource assignemnt policy class module
User
Administrator
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
0.9/1.0
Administrator can create assignment policy for computational and network resources programmablly through a ruby script.
OpenFlow Protocol
NMM allocates Flow Entries as network paths to a job based on resource assignment policy.
OpenFlow network
Job
Job
Job
Queue
JMS(OGS/GE)
#!/bin/csh
#$ -q QUEUE
#$ -pe ompi 4
#$ -l netprio=bandwidth mpirun -np 4 ./a.out
Job Script
User can also request network resources as well as computational resources in a job script.
[1] Y. Watashiba, Y. Kido, S. Date, H. Abe, K. Ichikawa, H. Yamanaka, E. Kawai, H. Takemura, "Prototyping and Evaluation of a Network-aware Job Management System on a Cluster System Leveraging OpenFlow", The 19th IEEE International Conference On Networks (ICON 2013), Dec. 2013.
Environment
Job Management System: Open Grid Scheduler / Grid Engine 2011.11p1
OpenFlow Controller: Trema 0.4.6 (OpenFlow Switch Specification 1.0.0)
OpenFlow Switch: NEC UNIVERGE PF5240 (VSI)