## Slide 1: Japan-Taiwan Satellite Image Transmission through PRAGMA Network testbed
Kohei Ichikawa (NAIST), Shinji Shimojo (Osaka University), Stoca Chang, Li-Chi Ku, Whey-Fone Tsai, Fang-Pang Lin (NCHC)

## Slide 2: Satellite Image Rapid Response to Disaster Event
Satellite image transmission for rapid response to natural disasters, such as tsunami and earthquake is very critical in Asia Pacific areas. JAXA, Japan and NSPO, Taiwan have planned for possible collaboration of multiple satellites.
Application case: Emergency Observation and Near real-time satellite image processing are critical for supporting to disaster response between Japan (Tsunami, Earthquake) and Taiwan (Flood, Landslide).
Complementary utilization of SAR (ALOS-2) (Operated by JAXA, Japan) and Optical (FORMOSAT-2) satellite image. (Operated by NSPO, Taiwan)
SAR
Optical

## Slide 3: Emergency Observation
Complementary utilization of SAR (ALOS-2) and Optical (FORMOSAT-2) satellite image
Rapid Response
  ALOS-2: accept EO request until one hour before observation, and provide data one hour after observation.
  FORMOSAT-2: accept EO request until 13:00, and provide data two hours after observation.
  Satellite Image transmission speed and efficiency in oversea affect the time of response to a natural disaster.
*Synthetic-aperture radar (SAR) is a form of radar which is used to create images of an object, such as a landscape. SAR can penetrate cloud during observation.

## Slide 4: Idea Plan (unofficial) for Satellite Image Receiving & Oversea Transmission for data sharing between two satellites.
NCHC
NAIST/Osaka U.
NSPO
Tokai U.
PRAGMA Network Testbed
Satellite image receiving
Satellite image receiving
First stage to test the performance of Network for image transmission between NAIST/Osaka U. and NCHC>

## Slide 5: Network Topology
Through PRAGMA-ENT testbed (end to end SDN)
TWAREN and JGN-X direct peering in Los Angeles
Using a dedicated 622 Mbps lightpath

## Slide 6: Satellite Image Transmission through PRAGMA Network Testbed
This DEMO connecting network between NAIST & Osaka U-Umeda and NCHC through access of the PRAGMA network testbed via TWAREN and TransPAC networks in oversea.
Formosat-2 Satellite images associated with 2011 Tohoku earthquake are used as the demo case for performance study of the network testbed.
Collaborators: Kohei Ichikawa (NAIST), Shinji Shimojo (Osaka U.), Stoca Chang (NCHC), Li-Chi Ku(NCHC), Whey-Fone Tsai (NCHC), Bo Chen (NSPO), Fang-Pang Lin (NCHC)

## Slide 7: Demo environment
Data plane
Slice plane
Virtual Network Slices
AutoVFlow
Japan&NCHC
AutoVFlow
UCSD
AutoVFlow
UF
AutoVFlow
User OpenFlow Controller
User OpenFlow Controller

## Slide 8: FS-2 IMAGE for Japan Earthquake
Method:
  rsync
Data set:
  Total size: 10.7 GB, 59 files.
Dataset details:
  1. Aomori(青森市): 5 files, 422 MB.
  2. GOI (五井,市原市): 1 file, 10.2 MB
  3. Japan Enhancement: 8 files, 6.18 GB.
  4. Iwate(岩手縣) : 39 files, 3.18 GB.
  5. Sendai(仙台市) : 6 files, 922 MB.

## Slide 9: Network speed test: CASE 1 (Internet)
NCHC -> NAIST
Data: 260 MB
Speed (Internet):
  2.06 MB/s
Time: 2min/10sec

## Slide 10: Network speed test: CASE 1 (Internet)
NCHC -> NAIST
Data: 10.7 GB
Speed (Internet):
  2.94 MB/s
Time: 1hour/3min/2sec

## Slide 11: Network speed test: CASE 2 (PRAGMA NETWORK TESTBED)
NCHC -> NAIST
Data: 3.54GB
Speed (PRAGMA):
  5.43 MB/s
Time
  10min/51.5sec

## Slide 12: Network speed test: CASE 2 (PRAGMA NETWORK TESTBED)
NAIST -> NCHC
Data: 442MB
Speed (PRAGMA):
  6.11 MB/s
Time
  72.49sec

## Slide 13
GOI (五井,市原市)
Japan enhancement
(Tsunami area)
Sendai