## Slide 1: An Implementation of SDN-enhanced Job Management System with Bandwidth Control
Yasuhiro Watashiba †1, Susumu Date †2, Hirotake Abe †3, Yoshiyuki Kido †2, Kohei Ichikawa †1, Hiroaki Yamanaka †4, Eiji Kawai †4, Shinji Shimojo †2,4 and Haruo Takemura †2
†1 Nara Institute of Science and Technology, Japan
†2 Osaka University, Japan
†3 University of Tsukuba, Japan
†4 National Institute of Information and Communications Technology (NICT), Japan

## Slide 2: Background
Current high-performance computing environment
  The dominant trend is cluster system.
Performance improvement
  Increase of computing nodes => large-scale and distributed
Structure of interconnect
  Interconnect also becomes large-scale and complex for achieving high communication performance and fault tolerant.
85.8%
14.2%
Architecture System Share
Cluster
MPP
Statistics of TOP500 Supercomputer Sites (November 2014)
Interconnect
Notes: High-performance computing as a cloud service which allows many users to benefit from a large-scale computing system.
Most of these computing environment are cluster system which are composed of multiple computers connected with interconnect.
Therefore, efficient resource allocation to user-requested computations on cluster system is essential for gaining high computational performance.

## Slide 3: Management on HPC environment
インターコネクト
Efficient and flexible resource management on cluster system is essential for gaining high computational performance.
高性能計算環境
Efficient execution of parallel and distributed computation for gaining high computational performance.
Management and handling of various resources and computational request.
Efficient system operation by running multiple jobs concurrently.
job
job
job

## Slide 4: Traditional Resource Management
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
0.9/1.0
User
JMS(OGS/GE)
Job
Queue
#!/bin/csh
#$ -q QUEUE
#$ -pe orte 4
… run program …
User can only request computational resources in a job script.
Job
script
interconnect
Job Management System (JMS)
  Traditional Resource Management System on HPC cluster systems
  Managing and allocating only computational resources.
JMS manages only computational resources in computing nodes.
JMS cannot handle interconnect as network resources.
The deployment of jobs is not considered about the topology and usage of interconnect.
A mechanism to handle interconnect as network resources is necessary.
Notes: In the field of HPC, Job Management System is responsible for managing and allocating resources of cluster system due to computational workload distribution and balancing.
This system handles a user-requested computation as a job.
Most of JMSs allocate resources of cluster system to each job only based on the usage of computational resources.
So JMS cannot manage an interconnect of cluster system as network resources, and users cannot also request network resources suitable the communications of a job.
As a result, the deployment of jobs is not always efficient in terms of network usage.

## Slide 5: SDN-enhanced JMS
  Leveraging Software Defined Networking / OpenFlow
  Retrieving topology and usage of interconnect
  Managing communication paths assigned to each job as Flow Entries
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
Network resource management under OpenFlow
  Network flow control
  Network resource Information retrieval
Network Management Module (NMM)
Database
Brain
Network Control
OpenFlow Controller (Trema)
SDN-enhanced JMS Framework
Resource Assignment Policy Class Module
User
job
job
job
Queue
JMS (OGS/GE)
Computing resource Management
#!/bin/csh
#$ -q QUEUE
#$ -pe ompi 4
#$ -l netprio=bandwidth
mpirun -np 4 ./a.out
Job Script
User can request network resources by requiring the policy name.
Administrator
Resource
Assignment
Policy
Brain decides computational and network resources to allocate to the job according to resource usage and resource assignment policy.
Administrator can create resource assignment policy for computational and network programmablly through a ruby script.
0.9/1.0
Notes: We have been developing the SDN-enhanced JMS by leveraging the functions of OpenFlow.
This shows the architecture of the SDN-enhanced JMS framework.
The Network Management Module, in which functionalities for managing and allocating network resources are equipped, is designed and implemented as an external module to the traditional JMS.
The NMM is composed of three components: the network control component, the brain component, and the database.
The network control component offers two functionalities:
retrieving information of the network resources and allocating communication paths to a job.
The brain component has a role of determining a suitable set of computational and network resources according to their usage information and resource assignment policy.
SDN-enhanced JMS allows an administrator to define how to allocate both computational and network resources to jobs in accordance with system architecture and operating policy.
Therefore, it is necessary to make a resource assignment policy suitable for the architecture of the cluster system.

## Slide 6: SDN-enhanced JMS
  Leveraging Software Defined Networking / OpenFlow
  Retrieving topology and usage of interconnect
  Managing communication paths assigned to each job as Flow Entries
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
Network resource management under OpenFlow
  Network flow control
  Network resource Information retrieval
Network Management Module (NMM)
Database
Brain
Network Control
OpenFlow Controller (Trema)
SDN-enhanced JMS Framework
Resource Assignment Policy Class Module
User
job
job
job
Queue
JMS (OGS/GE)
Computing resource Management
#!/bin/csh
#$ -q QUEUE
#$ -pe ompi 4
#$ -l netprio=bandwidth
mpirun -np 4 ./a.out
Job Script
User can request network resources by requiring the policy name.
Administrator
Resource
Assignment
Policy
Brain decides computational and network resources to allocate to the job according to resource usage and resource assignment policy.
Administrator can create resource assignment policy for computational and network programmablly through a ruby script.
0.9/1.0
- Available bandwidth of communication paths allocated to jobs is not guaranteed
- Handling only physical computational resources
Notes: However, if a network link is shared by communications generated by different jobs, the SDN-enhanced JMS cannot guarantee the available bandwidth on communication paths assigned to a job.
Though the available bandwidth should be allocated to each job based on user request and job priority, the SDN-enhanced JMS does not have any mechanisms to control the bandwidth of each communication on the network link.
Moreover, since computational resources are managed by the functionalities of the traditional JMS, the SDN-enhanced JMS cannot deploy job processes to virtual computational resources.

## Slide 7: Proposed resource management
  Allocation of virtual computational resources to a job
  QoS control by leveraging functions of Open vSwitch
Network Management Module (NMM)
DB
Brain
Network Control
OpenFlow Controller (Trema)
SDN-based JMS Framework
Resource assignemnt policy class module
User
Administrator
VM images
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
0.9/1.0
Vitrual resource management module
Open vSwitch
Computing host
VM
VM
VM
J o b
J o b
Administrator can create assignment policy for computational, network and virtual resources programmablly through a ruby script.
OpenFlow Protocol
NMM allocates Flow Entries as network paths to a job based on resource assignment policy.
OpenFlow network
QoS control by leveraging functions of Open vSwitch.
Process of a job is allocated and execute on VM automatically.
Job
Job
Job
Queue
JMS(OGS/GE)
Job Script
User can also request necessary bandwidth and VM image by describing in a job script.
For QoS Control Functions
Policy
Notes: In this approach, we propose the SDN-enhanced JMS equipped the mechanism to allow users to request job execution on virtual computational resources and available bandwidth on network resources allocated to a job.
In order to manage the bandwidth utilized by each job, we adopt QoS rate limit functions of Open vSwitches (OVSs).

## Slide 8: System architecture
Computing node
J o b
execd
shepherd
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
0.9/1.0
OpenFlow network
Network Management Module (NMM)
Database
Brain
Network Control
OpenFlow Controller (Trema)
SDN-enhanced JMS Framework
Resource assignment policy class module
User
Administrator
VM images
Computing node
J o b
“execd” calls “wrapper” instead of “shepherd”.
JMS(OGS/GE)
Flow entry
Resource
Assignment
Policy
qmaster
Job
execd
shepherd
wrapper
VM
Queue
Brain manages the allocation of virtual computational resources and the bandwidth controlled by Open vSwitch.
“wrapper” configures parameters of QoS functions on Open vSwitch, and boots up the VM with information to execute the job.
#!/bin/csh
#$ -q QUEUE
#$ -pe orte 4
#$ -l netprio=bandwidth #$ -l qos=1000 #$ -l vm=my-vm
… run program …
User can request resource assignment policy, bandwidth requirement and VM image.
Job
script
  Implementation of wrapper module
    Boot up user-request VM and deploy process of job on the VM
    Configure parameters of QoS functions on Open vSwitch
  QoS control by leveraging functions of Open vSwitch
Open vSwitch
Notes: For deploying the processes of a job on a user-requested VM, we develop the wrapper module to boot up the VM on each computing node and then to execute job on the VM.
This module also configures parameters of QoS functions on Open vSwitch according to user request.
In the poster presentation, we will show the architecture to utilize virtual computational resources and control available bandwidth by our SDN-enhanced JMS.
To run the wrapper is configured in shepherd_cmd.

## Slide 9: wrapper program
OGS/GE has a functionality for running a wrapper program for shepherd process.
Role of wrapper program
  Retrieving information for virtual machine and job management.
  Making CD image for guest OS on virtual machine
  Starting up virtual machine and running shepherd
  Configuring parameter of Open vSwitch
Tap is managed as slot.
Computing node
J o b
execd
shepherd
wrapper
VM
tap1
tap2
tap0
Open vSwitch

## Slide 10: Configure VM environment
Basic configuration for virtual machine is set up by auto-running CD image generated by SDN-enhanced JMS.
Contents of CD image
  option value for booting up virtual machine
  hostname
  size of memory
  network information (IP address, MAC addres, hosts)
  environment variable for SDN-enhanced JMS
Modify node list for parallel computation
  rename hostname of computing node to hostname of virtual machine

## Slide 11: Additional resource requirement
All of additional resource requirement are provided as “-l” options of qsub command.
Additional option
  netprio : type of network resource allocation ex) bandwidth, hop, and so on
  qosband : value of QoS rate limiting parameter in OpenvSwitch
  vmimage : Path of VM image.
  vmmemory: size of memory to allocate to VM
  vmopt : boot option of VM

## Slide 12: Demo environment
Constitution of cluster system
  The number of hosts: 28 nodes
  Network
    OpenFlow Switch : NEC UNIVERGE PF5240
    Bandwidth: 1Gbps

## Slide 13: Conclusion and Future work
This presentation shows implementation and behavior of SDN-enhanced JMS with the functionalities of managing virtual computational resources and bandwidth control.
Future work
  Development of resource assignment policy for handling these new resources
  Evaluation of effectiveness of these functionalities and new resource assignment policy

## Slide 14
Cluster system of Osaka University
  SDN-enhanced JMS will be deployed.
  This system will be connected with PRAGMA-ENT.
Home page http://hpc-sdn.ime.cmc.osaka-u.ac.jp/sdnjms/
  source code
  doccument

## Slide 15: Thank you for your attention !

## Slide 16: SDN / OpenFlow
Software-Defined Networking （SDN）
  Decomposing to control function and data transfer function
  Aggregating network management into a software application
SOpenFlow
  Implementation of the SDN concept
Ordinary network
OpenFlow Switch
OpenFlow Switch
OpenFlow Controller
OpenFlow Switch
OpenFlow protocol
OpenFlow Switch
OpenFlow network
Management
Management
Management
Management
Management
Flow entry
- Header Fields
- Actions
- Counters
Notes: For handling network resources on JMS, we focus on Software-Defined Networking enables flexible and dynamic management of the structure and configuration of a network..
In the SDN, the control function is decoupled from each network switch and then aggregated into a single controller.
SDN makes it possible to control network just like software programming in a centralized manner.
Therefore, we propose network-aware JMS leveraging OpenFlow which is an implementation of the SDN concept.

## Slide 17: Research goal
  Efficient and flexible resource management system
    Handling various computational and network resources.
Resource Management System
User
Administrator
job
job
job
Queue
JMS
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
0.9/1.0
Network Management module
Resource Assignment Policy
Vitrual resource management module
Virtual Switch
Computing host
VM
VM
VM
J o b
J o b
Allocation of virtual computational resources .
VM images
Administrator can create assignment policy for computational, network and virtual resources programmablly.
Resource control of communication path and bandwidth.
#!/bin/csh
#$ -q QUEUE
#$ -pe ompi 4
#$ -l netprio=bandwidth #$ -l qos=1000 #$ -l vm=my-vm
mpirun -np 4 ./a.out
Job Script
User can also request necessary bandwidth and VM image by describing in a job script.
Process of a job is allocated and execute on VM automatically.

## Slide 18: Proposed resource management
  Allocation of virtual computational resources to a job
  QoS control by leveraging functions of Open vSwitch
Network Management Module (NMM)
DB
Brain
Network Control
OpenFlow Controller (Trema)
SDN-based JMS Framework
Resource assignemnt policy class module
User
Administrator
VM images
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
0.9/1.0
Vitrual resource management module
Open vSwitch
Computing host
VM
VM
VM
J o b
J o b
Administrator can create assignment policy for computational, network and virtual resources programmablly through a ruby script.
OpenFlow Protocol
NMM allocates Flow Entries as network paths to a job based on resource assignment policy.
OpenFlow network
QoS control by leveraging functions of Open vSwitch.
Process of a job is allocated and execute on VM automatically.
Job
Job
Job
Queue
JMS(OGS/GE)
#!/bin/csh
#$ -q QUEUE
#$ -pe ompi 4
#$ -l netprio=bandwidth #$ -l qos=1000 #$ -l vm=my-vm
mpirun -np 4 ./a.out
Job Script
User can also request necessary bandwidth and VM image by describing in a job script.
For QoS Control Functions
Notes: In this approach, we propose the SDN-enhanced JMS equipped the mechanism to allow users to request job execution on virtual computational resources and available bandwidth on network resources allocated to a job.
In order to manage the bandwidth utilized by each job, we adopt QoS rate limit functions of Open vSwitches (OVSs).

## Slide 19: Architecture
Computing node
J o b
execd
shepherd
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
J o b
0.5/1.0
0.8/1.0
0.6/1.0
1.0/1.0
1.0/1.0
0.9/1.0
OpenFlow network
Network Management Module (NMM)
Database
Brain
Network Control
OpenFlow Controller (Trema)
SDN-enhanced JMS Framework
Resource assignment policy class module
User
Administrator
VM images
Computing node
J o b
“execd” calls “wrapper” instead of “shepherd”.
JMS(OGS/GE)
Flow entry
Resource
Assignment
Policy
qmaster
Job
execd
shepherd
wrapper
VM
Queue
Brain also manage the allocation of virtual computational resources and the bandwidth controlled by Open vSwitch.
“wrapper” configures parameters of QoS functions on Open vSwitch, and boots up the VM with information to execute the job.
#!/bin/csh
#$ -q QUEUE
#$ -pe orte 4
#$ -l netprio=bandwidth #$ -l qos=1000 #$ -l vm=my-vm
… run program …
User can request resource assignment policy, bandwidth requirement and VM image.
Job
script
  Implementation of wrapper module
    Boot up user-request VM and deploy process of job on the VM
    Configure parameters of QoS functions on Open vSwitch
  QoS control by leveraging functions of Open vSwitch
Open vSwitch
Notes: In this research, we propose the SDN-enhanced JMS equipped the mechanism to allow users to request job execution on virtual computational resources and available bandwidth on network resources allocated to a job.
In order to manage the bandwidth utilized by each job, we adopt Quality of Service (QoS) functions of Open vSwitches (OVSs).
For deploying the processes of a job on a user-requested VM, we develop the wrapper module to boot up the VM on each computing node and then to execute job on the VM.
This module also configures parameters of QoS functions on Open vSwitch according to user request.
In the poster presentation, we will show the architecture to utilize virtual computational resources and control available bandwidth by our SDN-enhanced JMS.
To run the wrapper is configured in shepherd_cmd.