## Slide 1: Extending the capability of TOUGHREACT simulator using parallel computing
Application to environmental problems

## Slide 2: What is TOUGHREACT ?
Multi-phase flow
+
Solute transport
+
Geochemical reaction
Coupled Process in porous media simulator,
developed in Lawrence Berkley Lab.

## Slide 3: Motivation of the work
Lab code constraints:
Developed for testing the model
Running on workstation or laptop
Numerical model can not scaling ( 8000 discrete grids limited)
Engineering requirements:
Carrying the simulation of site-scale model involved complex processes
Improve the speed in numerical solving .

## Slide 4: Method
Redevelop the software package using parallel computing schema.
Domain Decomposition.
Communication between divided subdomains(MPI)

## Slide 5: Domain Partition
ELEME A11 1 10.2000E+000.4000E+00 0.1000E+000.5000E+00-.5000E+00 A11 2 10.2000E+000.4000E+00 0.3000E+000.5000E+00-.5000E+00 A11 3 10.2000E+000.4000E+00 0.5000E+000.5000E+00-.5000E+00 A11 4 10.2000E+000.4000E+00 0.7000E+000.5000E+00-.5000E+00 CONNE A11 1A11 2 10.1000E+000.1000E+000.1000E+01 A11 2A11 3 10.1000E+000.1000E+000.1000E+01 A11 3A11 4 10.1000E+000.1000E+000.1000E+01
Multi-level Graph Partition:
Metis

## Slide 6: Parallel Linear Solver
Large Sparse Linear System iterative solving
Aztec

## Slide 7: Module organization
Public Module
Domain Decomposition
Parallel Matrices Assemble
IO
Parallel Linear solving
Subdomain Communication
Transport
Geochemical
Flow
Simulation procedure
EOS-MODULE
Index Transform-ation
State
Update

## Slide 8: Application: Carbon dioxide sequestration

## Slide 10
Fine grid model:
Total : 37824 grids

## Slide 11: Mid-term behavior prediction
Serial computing
Parallel Computing

## Slide 12: Runtime Statistics

## Slide 13: What we’ve gained from work
A new software package running on parallel computing facility ( Cluster …)
Speed up ( 20 X – 40 X in test case )
Simulation model scaling up ( 100,000 grids have been tested)

## Slide 14
Thanks for your attention !